## Slide 1: Two-Level Prediction Based Hybrid Transactional Memory
Yong Li
Song Zhang
Tianhao Zheng
Yuhao Zhu

## Slide 2: Introduction
What is Transactional Memory (TM)
Benefits of TM
  Ease parallel programming
  Parallel execution of transactions
Problems of TM
  Design complexity
  Performance issues
Our goal: improve STM performance

## Slide 3: Outline
Background and Motivation
Our Approach
  Two-level prediction adaptive scheme
Evaluation
Conclusion

## Slide 4: Background
HTM vs. STM
  HTM: faster but more complicated
  STM: flexible but slower
STM Algorithms
  Acquisition and Versioning
  Models & Algorithms (LLT)
Improve STM Efficiency
  Hybrid Approach
  Adaptive Approach

## Slide 5: Motivation
Observation
  Example: CounterBench in RSTM
TM vs. Lock:
  Speculation & Conflict vs. Stall & Conflict-free
Key: Better to stall than speculative if doomed to abort
Start from a STM Implementation
  Propose Conflict Prediction
  Accelerate STM in Hardware

## Slide 6: Two-Level Prediction Scheme
Goal: precisely predict if a transaction will be aborted later
First Level Prediction
  based on (coarse-grained) abort ratio information
  simple, fast, but less precise
Second Level Prediction
  based on (fine-grained) conflict history
  more accurate, but higher bookkeeping overhead

## Slide 7: First Level Predictor
Abort History Table (AHT)
  maintain per thread per transaction abort ratio
  maintain overhead negligible
Quick decision: Enter TM or NOT
  low abort ratio
    using LLT
  high abort ratio
    Second Level Prediction

## Slide 8: Second Level Predictor
To decide whether a thread should enter a TM even when the abort ratio is high
Hypothesis
  Two transactions are very likely to conflict with each other as long as they conflict once.
Three different schemes
  Brute Force Searching
  Simple Hashing
  Conflicted Cache

## Slide 9: Brute Force Searching
Two global structures:
  Conflict History Table (CHT)
    One entry for each transaction
    Each entry is a vector indicating the number of a particular transaction aborts current one
  Active Transaction Vector (AVT)
    One element for each transaction
    Each element is the number of threads currently executing the transaction

## Slide 10: Brute Force Searching (cont.)

## Slide 11: Brute Force Searching (cont.)
Prediction Scheme
  check corresponding entry in CHT
  for each element in the entry of CHT
    check whether the transaction is alive
  if any conflict transaction is alive
    stall the current thread, and keep pulling status of all conflict transactions until none of them is alive
  allow the thread to enter the transaction
Trade-offs
  Most accurate in prediction
  Unaffordable memory and computation overhead

## Slide 12: Simple Hashing
To tackle the overhead of brute force scheme
  map multiple different transactions into the same vector element in CHT entry
Trade-offs
  reduce entry size of CHT
  false positive

## Slide 13: Conflict Cache
Low Cost & Fast search
Most recently conflicted  Conflict cache
Indexed by the transaction id
Store transaction ids that previously aborted the indexed transaction (called conflicting txs)
If any conflicting tx is active (consulting ATV), stall the indexed transaction
Avoid false positive in simple hashing
Notes: As mentioned before, we ideally hope the table that store conflicts be low cost and can perform fast search.
It is similar to the context of cache.

## Slide 14: Conflict Cache
Logically set associative
Physically direct mapped
Notes: Logically, we design the conflict cache as an set associative cache. Thus can use different policy to maintain limited number of conflict transactions in the cache.
But physically, because transaction id is very short (e.g. one byte in our configuration). It is possible and better to assign all ways to one cache line to achieve parallel search.

## Slide 15: Conflict Cache
Replacement policy:
  LRC: Last Recently Conflict
T0 aborted by T2
T0 aborted by T1

## Slide 16: Conflict Cache
Performance
Cost
Temporal Locality
No false positive

## Slide 17: ISA Support
Two new instruction (to perform AHT, CHT, conflict cache, etc. manipulation)
  TM_Cond_Enter
  TM_End
New programming model
TM_Cond_Enter()
some TM transaction work...
TM_End()
Notes: TM_Cond_Enter hashes the current PC to a transaction ID to index various hardware tables (AHT, CHT, conflict cache etc.) depending on which level-2 prediction scheme to use. If the transaction is scheduled to execute (speculatively) according to our prediction, ATV will be updated to indicate that this transaction becomes active and the thread continues executing the rest instructions in the transaction. If a transaction is scheduled to stall, a conditional branch will point the control flow to the TM_Cond_Enter instruction again.

## Slide 18: Microarchitecture Support
Switch with thread

## Slide 19: Power, Area and Timing Estimation
CACIT 6.5
Configuration
Results

## Slide 20: Evaluation
Modified RSTM for software implementation
  LLT as the baseline
  Only libraries modified, no application source-level change required
  Carefully use fine-grained locks...
Evaluated on STAMP Benchmark
  Both high/low contention applications
  Both long/short transaction applications
24-core Xeon X5560 system
  4-socket, penalize lock synchronizations
  256 threads to create contentions; mean of 5 runs
RSTM: http://www.cs.rochester.edu/research/synchronization/rstm
STAMP: http://stamp.stanford.edu

## Slide 21: Evaluation
 | bayes | genome | intruder | kmeans1 | kmeans2 | vacation1 | vacation2 | ssca2
LLT | 79.2% | 2.51% | 1004% | 98.24% | 388.27% | 0.87% | 6.64% | 0.0067%
Two-level | 3.39% | 0.47% | 8.01% | 7.31% | 8.91% | 0.49% | 1.56% | 0.00043%
Abort Rate
Two-level prediction effectively reduces the abort rate significantly

## Slide 22: Evaluation
Execution time normalized to LLT

## Slide 23: Evaluation
Brute force overhead generally is unaffordable
Very few transactions
Very long transactions
Very high contention (79.2%)

## Slide 24: Evaluation
Simple hashing reduces searching overhead
False Positive!

## Slide 25: Evaluation
Pure conflict cache only checks most recently conflicted transactions
No Temporal Locality!

## Slide 26: Evaluation
Two-level scheme generally outperforms LLT
Very low contention (0.0067%)
Very short transactions

## Slide 27: Conclusion
We asked a fundamental question: when do we choose between transactional memory and locks?
Better to stall a transaction if it will be aborted later
We proposed a two-level prediction strategy that dynamically adapts between TM and locks
Our pure STM implementation achieves 17.2% improvement on high-contention applications
Preliminary analysis also shows hardware acceleration is promising

## Slide 28
Thanks!

## Slide 29: Evaluation
Dual core: less contention